## Slide 1: From Theory to Code: Fixed-Point FIR Filter Design and Speech Quality Evaluation
Saikiran Chepa

## Slide 2: Finite Impulse Response (FIR) Filter Design
Linear-phase design (symmetrical coefficients)
Always stable (no feedback terms)
Output depends only on current and past inputs
General Equation:
where:
= filter coefficients
= input signal
= output signal
= number of taps

## Slide 3: How to do Convolution??
Direct Convolution
  Multiply-accumulate (MAC) for each output sample
  Complexity: O(N·M) (N = input length, M = filter length)
  Simple but expensive for large filters
Overlap-Add (OLA)
  Input split into blocks
  Each block convolved using FFT
  Results added with overlap
  Efficient for long filters
Overlap-Save (OLS)
  Input divided into overlapping blocks
  FFT-based convolution, discarding invalid samples
  Memory-efficient alternative to OLA

## Slide 4: Overlap-Add(OLA)

## Slide 5: Overlap-Save(OLS)

## Slide 6: Design Steps:
Specification – Define filter type (Low-pass, High-pass, Band-pass, Band-stop)
Select Parameters –
  pass band frequency
  stop band frequency
  pass band ripple
  stop band attenuation
Compute Coefficients – Using mathematical formulas (sinc + window) or tools (MATLAB/Python remez)
Implementation – Use convolution in C/Python (float or fixed-point)
Verification – Compare float vs fixed output (RMSE, PESQ for speech signals)

## Slide 7: Motivation for Fixed Point
Why fixed-point?
  Lower power, smaller memory footprint
  Faster execution on embedded DSP/MCU
  Hardware limitations (many DSPs lack floating-point units)
Typical applications: Speech/audio codecs, filters

## Slide 8
Quantizer Types: Mid-Rise and Mid-Tread

## Slide 9: Floating-Point Representation (Refresher)
IEEE 754 format (32-bit float):
  Sign bit (1)
  Exponent (8)
  Mantissa (23)
Advantages: wide dynamic range, easy for algorithm development
Limitation: not always efficient for embedded

## Slide 10: Fixed-Point Representation
Represented as integers scaled by a factor
General format: Q1.m.n
  1 sign bit
  m = Range bits
  n = fractional bits
Example: Q1.0.15 (16-bit signed fixed-point)
  Range: –20 to (20 – 2⁻¹⁵) = -1.0 to 1 - 2⁻¹⁵
  Stored as 16-bit signed integer

## Slide 11: Float-to-Fixed Conversion
Formula:Q1.m.n
where n = number of fractional bits
Example:
  Float = 0.4768, Q1.0.15 → round(0.4768 × 215) = 15628
  Float = –0.5792, Q1.0.15 → round(- 0.5792 × 215) = –18979

## Slide 12: Precision vs. Range Trade-off
More fractional bits → higher precision, smaller range
  Q1.2.13 --> range is 22 --> -4 to 4 – 2-13 (0.0001220703125)
  Q1.2.29 --> range is 22 --> -4 to 4 – 2-29 (0.00000000186264514923095703125)
More integer bits → larger range, lower precision
Balance depends on algorithm

## Slide 13: Fixed-Point Arithmetic Examples
Addition/Subtraction → straightforward, same Q format
  How to add Q1.2.13 and Q1.3.12??
Multiplication → Q1.m.n × Q1.m.n = Q2.2m.2n → need to re-scale
Division → expensive, often replaced with reciprocal + multiply

## Slide 14: Practical Example
Total FIR Filter Coefficients is 13
Coefficients : max 2.786655772180386
Coefficients : min -2.9153372837924336
All Coefficients absolute sum: 23.597984136187275
How will you decide Q format for Coefficients??

## Slide 15: Verification
Compare float vs fixed-point FIR outputs
Metrics: RMSE, PESQ score for speech signals
PESQ score → indicates perceptual quality difference

## Slide 16: Summary
Float is convenient for design, fixed-point is efficient for embedded
Conversion involves scaling, rounding, and Q-format handling
FIR filters can be effectively implemented in fixed-point
Verification tools (PESQ, RMSE) ensure correctness

## Slide 17: Hands On
Fir Filter designed in Python, and coefficients and input signal dumped to binary files.
Implement floating point FIR Filter in C using the above coefficients and input signal.
Implement Fixed Point C code for FIR Filter.
Verify the outputs of Python and C Code using RMSE and PESQ.