## Slide 1
Saikiran Chepa
From Theory to Code Fixed-Point FIR Filter Design and Output Quality Evaluation

## Slide 2
Contents
Floating-Point Representation (Refresher)
Fixed-Point Representation
2.
1.
Finite Impulse Response (FIR) Filter Design
Motivation for Fixed Point
3.
4.
Fixed-Point Arithmetic Examples
Float-to-Fixed Conversion
5.
6.
Verification
Practical Example
7.
8.
Hands On
Summary
9.
10.

## Slide 3
01
Finite Impulse Response (FIR) Filter Design
PART

## Slide 4
Always stable (no feedback terms)
Output depends only on current and past inputs
01.
Linear-phase design (symmetrical coefficients)

## Slide 5
ℎ 𝑘 = filter coefficients
𝑦 𝑛 = output signal
M = number of taps
𝑥 𝑛 = input signal
01
02
03
04
General Equation:

## Slide 6
Input split into blocks Each block convolved using FFT Results added with overlap Efficient for long filters
Input divided into overlapping blocks FFT- based convolution, discarding invalid samples Memory- efficient alternative to OLA
Multiply- accumulate (MAC) for each output sample ComplexityO(N·M) (N = input length, M = filter length) Simple but expensive for large filters
Direct Convolution
Overlap-Add (OLA)
Overlap-Save (OLS)
How to do Convolution??

## Slide 7
1 | 2 | 3 | 4
Filter Coefficients
1 | 2 | 3 | 4
Frame 1
5 | 6 | 7 | 8
Frame 2
1 | 2
1 | 2
0 | 0 | 0 | 0 | 0
1 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 16
Delay Line
Output

## Slide 8
1 | 2 | 3 | 4
Filter Coefficients
1 | 2 | 3 | 4
Frame 1
5 | 6 | 7 | 8
Frame 2
1 | 2
1 | 2
0 | 1 | 2 | 3 | 4
1 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 16
Delay Line
Output
Y[0] = 1*1 + 2*0 = 1
2 | 1

## Slide 9
1 | 2 | 3 | 4
Filter Coefficients
1 | 2 | 3 | 4
Frame 1
5 | 6 | 7 | 8
Frame 2
1 | 2
1 | 2
0 | 1 | 2 | 3 | 4
1 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 16
Delay Line
Output
Y[1] = 1*2 + 2*1 = 4
2 | 1

## Slide 10
1 | 2 | 3 | 4
Filter Coefficients
1 | 2 | 3 | 4
Frame 1
5 | 6 | 7 | 8
Frame 2
1 | 2
1 | 2
0 | 1 | 2 | 3 | 4
1 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 16
Delay Line
Output
Y[2] = 1*3 + 2*2 = 7
2 | 1

## Slide 11
1 | 2 | 3 | 4
Filter Coefficients
1 | 2 | 3 | 4
Frame 1
5 | 6 | 7 | 8
Frame 2
1 | 2
1 | 2
0 | 1 | 2 | 3 | 4
1 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 16
Delay Line
Output
Y[3] = 1*4 + 2*3 = 10
2 | 1

## Slide 12
1 | 2 | 3 | 4
Filter Coefficients
1 | 2 | 3 | 4
Frame 1
5 | 6 | 7 | 8
Frame 2
1 | 2
1 | 2
0 | 1 | 2 | 3 | 4
1 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 16
Delay Line
Output

## Slide 13
1 | 2 | 3 | 4
Filter Coefficients
1 | 2 | 3 | 4
Frame 1
5 | 6 | 7 | 8
Frame 2
1 | 2
1 | 2
4 | 1 | 2 | 3 | 4
1 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 16
Delay Line
Output

## Slide 14
1 | 2 | 3 | 4
Filter Coefficients
1 | 2 | 3 | 4
Frame 1
5 | 6 | 7 | 8
Frame 2
1 | 2
1 | 2
4 | 5 | 6 | 7 | 8
1 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 16
Delay Line
Output

## Slide 15
1 | 2 | 3 | 4
Filter Coefficients
1 | 2 | 3 | 4
Frame 1
5 | 6 | 7 | 8
Frame 2
1 | 2
1 | 2
4 | 5 | 6 | 7 | 8
1 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 16
Delay Line
Output
Y[4] = 1*5 + 2*4 = 13
2 | 1

## Slide 16
1 | 2 | 3 | 4
Filter Coefficients
1 | 2 | 3 | 4
Frame 1
5 | 6 | 7 | 8
Frame 2
1 | 2
1 | 2
4 | 5 | 6 | 7 | 8
1 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 16
Delay Line
Output
Y[5] = 1*6 + 2*5 = 16
2 | 1

## Slide 17
1 | 2 | 3 | 4
Filter Coefficients
1 | 2 | 3 | 4
Frame 1
5 | 6 | 7 | 8
Frame 2
1 | 2
1 | 2
4 | 5 | 6 | 7 | 8
1 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 16
Delay Line
Output
Y[6] = 1*7 + 2*6 = 19
2 | 1

## Slide 18
1 | 2 | 3 | 4
Filter Coefficients
1 | 2 | 3 | 4
Frame 1
5 | 6 | 7 | 8
Frame 2
1 | 2
1 | 2
4 | 5 | 6 | 7 | 8
1 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 16
Delay Line
Output
Y[7] = 1*8 + 2*7 = 22
2 | 1

## Slide 19
1 | 2 | 3 | 4
Filter Coefficients
1 | 2 | 3 | 4
Frame 1
5 | 6 | 7 | 8
Frame 2
1 | 2
1 | 2
4 | 5 | 6 | 7 | 8
1 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 16
Delay Line
Output

## Slide 20
1 | 2 | 3 | 4
Filter Coefficients
1 | 2 | 3 | 4
Frame 1
5 | 6 | 7 | 8
Frame 2
1 | 2
1 | 2
8 | 5 | 6 | 7 | 8
1 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 16
Delay Line
Output

## Slide 21
1 | 2 | 3 | 4
Filter Coefficients
1 | 2 | 3 | 4
Frame 1
5 | 6 | 7 | 8
Frame 2
1 | 2
1 | 2
8 | 0 | 0 | 0 | 0
1 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 16
Delay Line
Output

## Slide 22
1 | 2 | 3 | 4
Filter Coefficients
1 | 2 | 3 | 4
Frame 1
5 | 6 | 7 | 8
Frame 2
1 | 2
1 | 2
8 | 0 | 0 | 0 | 0
1 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 16
Delay Line
Output
Y[8] = 1*0 + 2*8 = 16
2 | 1

## Slide 23
Impulse response: h[n], length = M + 1.
Input sequence: x[n], length = Nx.
Choose FFT size N ≥ L + M where:
L = block length of input,
Each input block has length L,
Output per block has length L + M.
Block 1: x[0] ... x[L - 1]
Block 2: x[L] ... x[2L - 1]
Block 3: x[2L] ...
Zero-pad each block to length .
Zero-pad to length .
Perform FFT of both, multiply in frequency domain,
IFFT → gives circular convolution.
Overlap and Add Method

## Slide 24
Handle overlap (why it’s called Overlap-Add):
Each block convolution produces samples.
When placing results together, the last samples
of one block overlap with the first samples of the
next block’s result.
So, we add them together.
Concatenate + Add overlaps:
Place outputs one after another, and wherever they overlap,
add the samples.
The final result = linear convolution .

## Slide 26
Y[n] = n=0,1,…,(N-1)
Key Points:
Signals are assumed periodic with period N.
Output length is always N.
Extra terms wrap around and add at the beginning of the output.
Circular Convolution

## Slide 27
Input block: x = [1,2,3,4] , length N = 4.
Filter: h = [1,1,1] , length M = 3
ylinear​ = [1,3,6,9,7,4]
Y[0] = x[0]*h[(0-0) mod N] + x[1]*h[[(0-1) mod N]+ x[2]*h[(0-2) mod N] + x[3]*h[[(0-3) mod N]
= 1*1+2*0+3*1+4*1 = 8
Y[1] = x[0]*h[(1-0) mod N] + x[1]*h[[(1-1) mod N]+ x[2]*h[(1-2) mod N] + x[3]*h[[(1-3) mod N]
= 1*1+2*1+3*0+4*1 = 7
Y[2] = x[0]*h[(2-0) mod N] + x[1]*h[[(2-1) mod N]+ x[2]*h[(2-2) mod N] + x[3]*h[[(2-3) mod N]
= 1*1+2*1+3*1+4*0 = 6
Y[3] = x[0]*h[(3-0) mod N] + x[1]*h[[(3-1) mod N]+ x[2]*h[(3-2) mod N] + x[3]*h[[(3-3) mod N]
= 1*0+2*1+3*1+4*1 = 9

## Slide 28
Input block: x = [1,2,3,4] , length N = 4.
Filter: h = [1,1,1] , length M = 3
ylinear​ = [1,3,6,9,7,4]
ycircular​[k] = ylinear​[k] + ylinear​[k + N], (k=0,1,2,3)
Compute explicitly:
: ycircular​
: ycircular​ =
: ycircular​ =
: ycircular​ =
So, the circular convolution output is:

## Slide 29
Let input sequence = x[n], n = 0,1,…,Nx−1
Filter impulse response = h[n], length M+1
Choose FFT size N such that N ≥ (M+1)
Each processed block will output N−M
Segment 1: x[0] ... x[N-1]
Segment 2: x[N-M] ... x[2N-M-1]
Segment 3: x[2N-2(M)] ...
Overlap and Save Method

## Slide 31
Compute FFT of each segment (length ).
Compute FFT of , zero-padded to length .
Multiply in frequency domain.
Perform IFFT to get time-domain result.
Each block produces output samples, but the first samples are invalid (they contain circular convolution wrap around).
Discard those.
The remaining samples are the valid part of the linear convolution.
Concatenate the valid samples from each block to reconstruct the full output .

## Slide 32
01
02
03
Specification
Define filter type (Low- pass, High- pass, Band- pass, Band- stop)
Implementation
Use convolution in C/Python (float or fixed- point)
Select Parameters
Pass band frequency Stop band frequency Pass band ripple Stop band attenuation
Verification
Compare float vs fixed output (RMSE, PESQ for speech signals)
Compute Coefficients
Using mathematical formulas (sinc + window) or tools (MATLAB/Python remez)
04
05
Design Steps

## Slide 33
02
Floating-Point Representation (Refresher)
PART

## Slide 34
Sign bit (1)
Advantages wide dynamic range, easy for algorithm development
Exponent (8)
Limitation not always efficient for embedded
Mantissa (23)
01
02
03
04
05
IEEE 754 format (32-bit float)

## Slide 35
03
Motivation for Fixed Point
PART

## Slide 36
Lower power, smaller memory footprint
Hardware limitations (many DSPs lack floating- point units)
Faster execution on embedded DSP/MCU
Typical applicationsSpeech/audio codecs, filters
Why fixed-point?

## Slide 37
Quantizer Types: Mid-Rise and Mid-Tread

## Slide 38
04
Fixed-Point Representation
PART

## Slide 39
sign bit
m = Range bits
n = fractional bits
General format: Q1.m.n

## Slide 40
Q1.0.15 : Range –20 to (20 – 2⁻¹⁵) = - 1.0 to 1 - 2⁻¹⁵
Stored as (1+m+n)- bit signed integer
Example: Q1.0.15 (16-bit signed fixed-point)

## Slide 41
05
Float-to-Fixed Conversion
PART

## Slide 42
02
Example 2Float = –0.5792, Q1.0.15 → round(–0.5792 × 2¹⁵) = –18979
01
Example 1Float = 0.4768, Q1.0.15 → round(0.4768 × 2¹⁵) = 15624
Formula: Q1.m.n Fixedpt_value = round (Floatingpt_value × 2ⁿ)

## Slide 43
02
Example 2Float = –5.5872, Q1.3.12 → round(–5.5872 × 212) = -22885
01
Example 1Float = 2.4897, Q1.2.13 → round(2.4897 × 213) = 20396
Formula: Q1.m.n Fixedpt_value = round (Floatingpt_value × 2ⁿ)

## Slide 44
More fractional bits → higher precision, smaller range
More integer bits → larger range, lower precision
Balance depends on algorithm
Precision vs. Range Trade-off

## Slide 45
06
Fixed-Point Arithmetic Examples
PART

## Slide 46
Straightforward, same Q format
01
Addition/Subtraction

## Slide 47
Will you convert Q1.2.13 to Q1.3.12?? Or Will you convert Q1.3.12 to Q1.2.13??
How to add Q1.2.13 and Q1.3.12??

## Slide 48
Q1.m.n × Q1.m.n = Q2.2m.2n → need to re- scale
Multiplication

## Slide 49
Expensive, often replaced with reciprocal + multiply
Division

## Slide 50
Understanding Precision and Range in Fixed-Point Representation

## Slide 51
Integer Bits and Range
2.
1.
Fractional Bits and Precision
Contents
Balancing Precision and Range
3.

## Slide 52
Fractional Bits and Precision
01
PART.

## Slide 53
Increasing the number of fractional bits enhances the accuracy of numerical representation, allowing for more precise calculations, which is crucial in fields requiring detailed data.
Higher Precision Explained
The Q1.2.13 format provides limited precision compared to Q1.2.29, illustrating how the additional fractional bits in Q1.2.29 capture finer details in numerical values, affecting data integrity.
Example: Q1.2.13 vs. Q1.2.29
Impact of More Fractional Bits

## Slide 54
02
01
Range Limitations
As more fractional bits are added, the range of representable values can decrease, leading to potential underflow or overflow issues that limit practical data use in various applications.
Real-world Applications
In engineering and computer graphics, the balance between precision and range is essential, influencing how data is processed and displayed in tools such as CAD software and gaming engines.
Trade-offs in Precision

## Slide 55
Integer Bits and Range
02
PART.

## Slide 56
Increasing the number of integer bits allows for a greater range of values, enabling computers to accurately represent larger numbers without overflow, which is crucial for complex calculations.
Larger Range Benefits
In data representation, more integer bits can store larger integers, enhancing performance in applications like gaming and data analysis where numerical limits are often a concern.
Examples in Data Representation
Importance of More Integer Bits

## Slide 57
Decreased Precision
While more bits increase the range, they can reduce precision in some contexts, affecting applications that rely on exact numeric representation, such as financial calculations.
.
Consequences of Increasing Integer Bits

## Slide 58
Balancing Precision and Range
03
PART.

## Slide 59
Algorithmic Dependencies
Algorithmic dependencies refer to how various algorithms interact with data. Understanding these relationships helps in achieving optimal performance in precision and range while avoiding errors.
Practical Considerations
Practical considerations involve real- world factors such as computational resources, data variability, and context of use, influencing how to balance precision and range effectively in algorithm design.
02
01
Understanding the Balance

## Slide 60
07
Practical Example
PART

## Slide 61
01
Coefficients max: 2.786655772180386
02
Coefficients min: -2.9153372837924336
03
All Coefficients absolute sum: 23.597984136187275
Total FIR Filter Coefficients is 13

## Slide 62
How will you decide Q format for Coefficients??

## Slide 63
08
Verification
PART

## Slide 64
Metrics RMSE, PESQ score for speech signals
PESQ score → indicates perceptual quality difference
Compare float vs fixed-point FIR outputs

## Slide 65
09
Summary
PART

## Slide 66
10
Hands On
PART

## Slide 67
Thanks
PowerPoint Design